## Slide 1
SAFEG AI
Customer Onboarding &
Camera Integration Guide
Complete step-by-step implementation guide for factory safety AI deployment
22 Cameras Supported
6-Step Process
< 1 Day Setup
LIVE FEEDS
Version 1.0 · 2025 · Confidential
1 / 22

## Slide 2
SAFEG AI
2 / 22
What's Inside
01
Welcome & Overview
What SafeG AI does for your factory
02
Pre-Installation Checklist
Network, hardware & site requirements
03
Account Setup & Wizard
Registration, plant, zones & user roles
04
Camera Installation
Mounting, cabling, RTSP config per zone
05
AI Configuration & Testing
Detection rules, sensitivity, alerts
06
Go-Live & Support
Dashboard, Form 18, WhatsApp alerts, SLA

## Slide 3
01
Welcome &
Overview
Understanding SafeG AI before you begin
SAFEG AI
SECTION 01 — OVERVIEW
3 / 22

## Slide 4
SAFEG AI
01 — OVERVIEW
4 / 22
OVERVIEW
What SafeG AI Does For Your Factory
📷
Real-Time PPE Detection
AI watches every camera 24/7, detecting missing helmets, vests, boots, gloves and eye protection in < 3 seconds.
⚠️
Instant Violation Alerts
WhatsApp + Email alerts reach your HSE team within 28 seconds of detection. No delayed reports.
📋
Form 18 Auto-Fill
94% of Factories Act Form 18 fields auto-populated from AI detections. Inspector-ready reports.
📊
Compliance Dashboard
Live KPIs, 7-day trends, PPE compliance rates and violation heatmaps for every zone.
🔒
Danger Zone Monitoring
Virtual perimeters around hazardous areas. AI raises alert the moment an unauthorised worker enters.
🏭
Multi-Plant Support
Single dashboard for up to 32 cameras across 5 plants. Role-based access for HSE officers and managers.

## Slide 5
SAFEG AI
01 — OVERVIEW
5 / 22
OVERVIEW
Impact at a Glance
Typical results within 90 days of deployment
73%
Reduction in
PPE Violations
< 3s
AI Detection
Latency
98.7%
Detection
Accuracy
< 6 mo
Payback
Period
From camera to alert in under 30 seconds
Camera Captures Frame
AI Analyses PPE
Violation Detected
Alert Sent
Dashboard Updated

## Slide 6
02
Pre-Installation
Checklist
Everything you need ready before Day 1
SAFEG AI
SECTION 02 — PRE-INSTALLATION
6 / 22

## Slide 7
SAFEG AI
02 — PRE-INSTALLATION
7 / 22
PRE-INSTALL
Network & Infrastructure Requirements
🌐 NETWORK
Internet: Min. 10 Mbps upload (25 Mbps recommended)
Local LAN: 100 Mbps switch (Gigabit preferred)
IP Range: 192.168.x.x dedicated VLAN for cameras
Ports open: RTSP 554, HTTP 80/443, WebSocket 4000
Static IPs for each camera (DHCP reservation OK)
VPN or firewall whitelist for SafeG AI cloud: api.syyaimsafeg.ai
UPS backup power on PoE switch (min. 4-hour runtime)
🖥 HARDWARE
IP Cameras: 2MP+ resolution, RTSP support, H.264/H.265
PoE Switch: 30W per port for PTZ, 15W for fixed cams
Edge Server (optional): Intel i5/i7 NUC, 16GB RAM, SSD
NVR (optional): 4-channel minimum for local recording
Cat6 cable: max 100m per camera run
Conduit: PVC/metal for outdoor cable routing
Junction boxes: IP66 rated for outdoor installations

## Slide 8
SAFEG AI
02 — PRE-INSTALLATION
8 / 22
PRE-INSTALL
Site Survey Checklist
Complete this survey at least 7 days before installation date
Zone Identification
Map all hazardous zones on factory floor plan
Count workers per shift per zone
Identify PPE requirements for each zone
Mark danger zones and restricted areas
Camera Coverage Planning
Identify mounting positions (walls, pillars, gantries)
Check ceiling/mount height (3m–8m ideal)
Confirm field of view covers work area
Note lighting conditions (supplementary lighting needed?)
Power & Cabling
Locate nearest power source per camera position
Measure cable runs (note obstructions)
Check conduit routing path
Confirm PoE switch location and capacity
Connectivity
Test internet speed at server room
Confirm network switch port availability
Get IT approval for VLAN/firewall changes
Identify PC/server for SafeG AI edge node
📥 Download the full Site Survey form: support.syyaimsafeg.ai/survey · Or request via WhatsApp: +91 98765 43210

## Slide 9
03
Account Setup &
Onboarding Wizard
Creating your plant, zones and user accounts
SAFEG AI
SECTION 03 — ACCOUNT SETUP
9 / 22

## Slide 10
SAFEG AI
03 — ACCOUNT SETUP
10 / 22
ACCOUNT SETUP
The 5-Step Onboarding Wizard
Visit app.syyaimsafeg.ai → Sign Up → Complete the wizard below
1
Company Details
Company name & CIN
Industry type
Employee count
Contact person & GSTIN
2
Plant Information
Plant name & address
Factory Licence No.
HSE Officer details
GPS coordinates
3
Zone / Area Setup
Add each zone (Welding, Assembly…)
Set risk level per zone
Define PPE requirements
Enable danger zone flag
4
Camera Registration
Camera ID & location
RTSP URL or IP address
Mount height & angle
AI detection rules
5
Activate SafeG AI
Review all settings
One-click activation
Cameras go live
Welcome email sent
⏱ Total wizard time: approximately 15–20 minutes with all information ready

## Slide 11
SAFEG AI
03 — ACCOUNT SETUP
11 / 22
ACCOUNT SETUP
User Roles & Access Levels
ADMIN
Customer Admin
Full access — billing, users, all plants, AI config
✓ Create/delete users
✓ Manage billing
✗ System config (SafeG team only)
MANAGER
Plant Manager
All features for assigned plant(s) — read/write
✓ Camera management
✓ View all violations
✗ Billing & subscription
✗ Create new plants
HSE
HSE Officer
Violations, Form 18, inspections — read/write
✓ Acknowledge violations
✓ Fill Form 18
✗ Camera config
✗ User management
OPS
Operator
View dashboard and live feeds only — read only
✓ Live camera feeds
✓ Dashboard KPIs
✗ Acknowledge/resolve violations
✗ Any settings

## Slide 12
04
Camera Installation
Step-by-Step
Mounting, cabling, IP config and RTSP setup for every zone type
SAFEG AI
SECTION 04 — CAMERA INSTALLATION
12 / 22

## Slide 13
SAFEG AI
04 — CAMERA INSTALLATION
13 / 22
CAMERA INSTALL
Camera Placement Guide by Zone Type
⚡ Welding Bay
Height:
4–6m
Angle:
30–45°
Coverage:
One per 150 sq.ft
💡 Use dust-resistant IP67 camera + spark deflector hood
⚙️ Assembly Line
Height:
3–5m
Angle:
15–30°
Coverage:
One per 20m of line
💡 Ensure adequate lighting ≥ 300 lux. Avoid backlighting.
🧪 Paint / Chemical
Height:
3–4m
Angle:
20–35°
Coverage:
Two cameras per bay
💡 Use explosion-proof camera (Zone 2 rated) in spray booths.
🚛 Forklift / Dock
Height:
5–8m
Angle:
45–60°
Coverage:
Corner mounts preferred
💡 PTZ camera recommended for large dock areas > 500 sq.ft.
🔧 Machine Shop
Height:
3–4m
Angle:
20–40°
Coverage:
One per 4 machines
💡 Install IR illuminator if area has variable lighting shifts.
⚡ Electrical Room
Height:
2.5–3m
Angle:
Wide
Coverage:
One covers entire room
💡 Standard IP66 camera sufficient — no heavy dust/fumes.

## Slide 14
SAFEG AI
04 — CAMERA INSTALLATION
14 / 22
CAMERA INSTALL
Physical Installation — Step by Step
1
Mark Mounting Position
Use laser level. Mark drill holes. Check for hidden wiring/pipes with stud finder. Install wall anchor or pipe clamp.
2
Route & Lay Cable
Pull Cat6 cable from camera position to PoE switch. Max 90m. Use conduit/cable trays. Label both ends (e.g. CAM-01-A).
3
Mount Camera Bracket
Secure bracket to wall/pillar. Tighten all bolts. For outdoor: apply waterproof sealant around drill holes.
4
Connect & Power On
Terminate Cat6 to camera (T568B standard). Connect to PoE switch port. Camera LED turns on in 15–30 seconds.
5
Set Static IP Address
Access camera web UI at 192.168.1.x (default). Set static IP per naming plan. Example: CAM-01 → 192.168.10.101.
6
Adjust Pan/Tilt/Zoom
View live feed via camera web UI. Adjust angle to cover full work zone. Lock screw when satisfied.
7
Record RTSP URL
Format: rtsp://admin:PASSWORD@192.168.10.101:554/stream1 Note this down — you'll enter it in SafeG wizard.
8
Label & Document
Stick asset label on camera (CAM-01, zone, IP). Update site floor plan with camera positions.

## Slide 15
SAFEG AI
04 — CAMERA INSTALLATION
15 / 22
RTSP CONFIG
RTSP URL & IP Configuration Reference
RTSP URL Anatomy
rtsp://
admin:password
@
192.168.10.101
:554/
stream1
Protocol
Credentials
Camera IP
Port/Path
RTSP Stream Paths by Camera Brand
Brand | RTSP URL Pattern | Stream
Hikvision | rtsp://admin:PASS@IP:554/Streaming/Channels/101 | Main stream
Dahua | rtsp://admin:PASS@IP:554/cam/realmonitor?channel=1&subtype=0 | Main HD
Axis | rtsp://root:PASS@IP/axis-media/media.amp | VAPIX stream
Hanwha/Samsung | rtsp://admin:PASS@IP/video1 | H.264 main
CP Plus (CPDI) | rtsp://admin:PASS@IP:554/live/ch00_0 | Main stream
Bosch | rtsp://IP:554/rtsp_tunnel?h26x=4&line=1&inst=1 | H.264 main
Generic ONVIF | rtsp://admin:PASS@IP:554/onvif1 | Standard path

## Slide 16
SAFEG AI
04 — CAMERA INSTALLATION
16 / 22
CAMERA INSTALL
IP Addressing & Camera Naming Convention
Recommended IP Addressing Scheme
SafeG AI Edge Server:
192.168.10.10
PoE Switch Management:
192.168.10.1
Cameras (Unit 1):
192.168.10.101 – .132
Cameras (Unit 2):
192.168.10.133 – .164
NVR (if used):
192.168.10.50
Subnet Mask:
255.255.255.0 ( /24 )
Default Gateway:
192.168.10.1
Camera Naming Convention
CAM-PLT-PUN-001-003
CAM =
Prefix
PLT =
Product
PUN =
City code
001 =
Plant seq.
003 =
Camera seq.
Typical PoE Wiring Diagram
IP Camera
(×8–32)
PoE Switch
(Gigabit)
Router /
Firewall
Edge Server
(SafeG AI)
SafeG AI
Cloud
Cat6 — 90m max
10/100/1000 LAN
Internet uplink

## Slide 17
05
AI Configuration
& Testing
Setting detection rules, sensitivity and alert routing per zone
SAFEG AI
SECTION 05 — AI CONFIGURATION
17 / 22

## Slide 18
SAFEG AI
05 — AI CONFIGURATION
18 / 22
AI CONFIG
Configuring AI Detection Rules Per Zone
PPE Detection Types
⛑
Hard Hat / Helmet
detect_helmet
ON
🦺
Safety Vest / Hi-Viz
detect_vest
ON
👟
Safety Boots
detect_boots
OFF
🥽
Eye Protection
detect_eye
OFF
🧤
Gloves
detect_gloves
OFF
🎧
Ear Protection
detect_ear
OFF
🚧
Danger Zone Breach
detect_danger
ZN
📡
Motion Detection
detect_motion
ON
Alert Sensitivity
HIGH
Alert on every detection
Best for: Welding, Chemical zones
MEDIUM
Alert after 2+ detections
Best for: Assembly, Machine shop
LOW
Alert on repeated violations
Best for: Office, Canteen entry
Alert Routing Configuration
📱 WhatsApp:
Add HSE mobile numbers → messages.syyaimsafeg.ai
📧 Email:
Add multiple email IDs in Settings → Alerts → Email recipients
🖥️ Dashboard:
All violations auto-appear in live dashboard — no config needed
📋 Form 18:
Violations auto-populate Factories Act Form 18 — review weekly

## Slide 19
SAFEG AI
05 — AI CONFIGURATION
19 / 22
TESTING
Pre-Launch Testing & Validation Checklist
Camera Connectivity Tests
All cameras show 'Online' status in dashboard
Live feed visible for each camera (no black screens)
Resolution confirmed: min. 720p (1080p recommended)
Frame rate ≥ 3.5 FPS sustained under load
RTSP stream reconnects automatically after network drop
AI Detection Accuracy Tests
Walk through each zone wearing PPE — no false violation
Remove hard hat — violation detected within 3 seconds
Remove vest — violation detected and alert sent
Test danger zone: enter boundary → instant alert
Night / low-light test: detection works at shift change
Alert System Tests
Test WhatsApp: violation triggers message to HSE number
Test Email: receipt confirmed to all recipients
Dashboard violation counter increments correctly
Form 18 auto-populates from test violation
Acknowledge and resolve flow works end-to-end
User Access Tests
Admin: can access all plants and settings
HSE Officer: can acknowledge violations, cannot edit cameras
Operator: view-only dashboard, no settings visible
Password reset flow tested for all user roles
Session timeout works after inactivity period
✅ All tests passed = System is ready for Go-Live. SafeG AI team must countersign the acceptance form.

## Slide 20
06
Go-Live &
Ongoing Support
First day live, Form 18 workflow, and how to get help
SAFEG AI
SECTION 06 — GO-LIVE
20 / 22

## Slide 21
SAFEG AI
06 — GO-LIVE & SUPPORT
21 / 22
GO-LIVE
Go-Live Day & Form 18 Compliance Workflow
🚀 Go-Live Day Sequence
08:00
SafeG AI team performs final camera check
09:00
Activation button pressed — cameras go live
09:15
HSE Officer confirms WhatsApp alerts working
10:00
Full shift monitoring begins — first KPIs visible
16:00
End-of-shift review: violations, patterns, gaps
17:00
Form 18 first draft auto-generated — HSE reviews
📋 Form 18 Workflow
1
AI auto-fills 94% of fields
2
HSE Officer reviews & edits
3
Plant Manager approves
4
PDF generated — inspector-ready
5
Archive in SafeG reports vault
📞 Support Contacts & SLA
WhatsApp Support
+91 98765 43210
24 × 7
Email Support
support@syyaimsafeg.ai
< 4hr response
Onboarding CSM
Your dedicated manager
Business hours
Emergency Line
+91 98765 43220
Critical issues 24×7

## Slide 22
SAFEG AI
You're Ready to Go Live.
SafeG AI will now monitor your factory 24/7 — reducing PPE violations, simplifying compliance and keeping your workers safe.
🖥 Dashboard
app.syyaimsafeg.ai
🛟 Support
support.syyaimsafeg.ai
📚 Docs
docs.syyaimsafeg.ai
📱 WhatsApp
+91 98765 43210
Your SafeG AI onboarding team is available 24×7 during the first 30 days — call anytime.
Version 1.0 · Confidential · © 2025 Syyaim SafeG AI Pvt. Ltd.
22 / 22