## Slide 1
EXISTING CAMERAS
EXISTING CAMERA ONBOARDING
SafeG AI
Integration Guide
Connect your already-installed factory cameras to SafeG AI in one day —
no new hardware, no disruption to operations.
No New Hardware
< 1 Day Setup
Any Brand Camera
RTSP / ONVIF / SDK
Version 1.0 · Confidential · © 2025 Syyaim SafeG AI Pvt. Ltd.
1 / 24

## Slide 2
SAFEG AI
2 / 24
What This Guide Covers
01
Overview & How It Works
SafeG AI with your existing cameras
02
Pre-Integration Checklist
What you need before connecting
03
Camera Discovery & Audit
Inventory, RTSP discovery, compatibility check
04
SafeG AI Account & Wizard Setup
Company, plant, zones and camera registration
05
Connecting Cameras to SafeG AI
RTSP/ONVIF/SDK methods, brand-by-brand guide
06
Troubleshooting & Validation
Common errors, fixes and live-stream testing
07
AI Rules, Alerts & Go-Live
Detection config, WhatsApp alerts, Form 18

## Slide 3
01
Overview &
How It Works
SafeG AI activates on your existing camera infrastructure
SAFEG AI
SECTION 01 — OVERVIEW
3 / 24

## Slide 4
SAFEG AI
01 — OVERVIEW
4 / 24
OVERVIEW
How SafeG AI Works With Existing Cameras
📷
Your Existing
IP Cameras
Any brand
Hikvision·Dahua·Axis
Bosch·CP Plus·ONVIF
📡
RTSP / ONVIF
Stream
Network stream
over LAN — no
hardware added
🧠
SafeG AI
Edge / Cloud
Claude Vision AI
analyses frames
at 4 FPS
⚠️
Detection &
Alerting
Violations flagged
WhatsApp + Email
within 28s
📋
Dashboard &
Form 18
Live KPIs
Compliance reports
Inspection-ready
SafeG AI reads the RTSP video stream from your existing cameras — zero new wiring, zero camera replacement

## Slide 5
SAFEG AI
01 — OVERVIEW
5 / 24
OVERVIEW
Camera Compatibility — What We Support
✅ FULLY SUPPORTED BRANDS
Hikvision
RTSP · ISAPI SDK · ONVIF
✓ Tested
Dahua
RTSP · DHOP SDK · ONVIF
✓ Tested
Axis
RTSP · VAPIX API · ONVIF
✓ Tested
Bosch
RTSP · ONVIF Profile S
✓ Tested
CP Plus (CPDI)
RTSP · ONVIF
✓ Tested
Hanwha/Samsung
RTSP · Sunapi · ONVIF
✓ Tested
Uniview (UNV)
RTSP · ONVIF
✓ Tested
Reolink
RTSP (enable in camera settings)
✓ Tested
Generic ONVIF
ONVIF Profile S / T
✓ Supported
MINIMUM REQUIREMENTS
🎥
Resolution:
720p minimum
(1080p recommended)
📡
Protocol:
RTSP, ONVIF
or brand SDK
🖧
Network:
Camera on same LAN
as SafeG AI server
🔢
Frame Rate:
≥ 5 FPS live stream
(4 FPS used by AI)
🔐
Credentials:
Camera login (admin/
password) needed
💡
Lighting:
≥ 200 lux
IR OK for night

## Slide 6
02
Pre-Integration
Checklist
Gather everything you need before starting the connection process
SAFEG AI
SECTION 02 — PRE-INTEGRATION CHECKLIST
6 / 24

## Slide 7
SAFEG AI
02 — PRE-INTEGRATION CHECKLIST
7 / 24
PRE-INTEGRATION
What to Collect Before You Begin
📋 CAMERA INFORMATION
Camera make and model (for each camera)
Camera firmware version
Camera IP address (static or DHCP-reserved)
Admin username and password for each camera
RTSP port (default: 554) — confirm not changed
Number of cameras per zone/area
Mounting location and height notes
🌐 NETWORK INFORMATION
IP address range of camera VLAN/subnet
Network switch type and PoE details
Internet upload speed (min 10 Mbps)
Firewall rules — confirm port 554 open (RTSP)
NVR IP address (if cameras are behind an NVR)
Wi-Fi SSID (if any cameras are wireless)
VPN access details (if cameras on separate network)
🏭 PLANT INFORMATION
Plant name and full address
Factory Licence Number (Form 18)
Number of zones/areas (Welding, Assembly…)
PPE requirements per zone
HSE Officer name and mobile number
Plant Manager name and email
Number of workers per shift
💡 Tip: Download the Camera Inventory Sheet from docs.syyaimsafeg.ai to record all details before Day 1

## Slide 8
03
Camera Discovery
& Audit
Find every camera on your network, check compatibility and map them to zones
SAFEG AI
SECTION 03 — CAMERA DISCOVERY & AUDIT
8 / 24

## Slide 9
SAFEG AI
03 — CAMERA DISCOVERY
9 / 24
DISCOVERY
Step 1 — Discover All Cameras on the Network
METHOD A — SafeG AI Auto-Discovery (Recommended)
During the SafeG onboarding wizard, run the built-in camera scanner:
1
In the wizard → Camera Registration → Click 'Scan Network'
2
Enter your camera subnet: e.g. 192.168.10.0/24
3
Scanner finds all RTSP/ONVIF devices and lists their IPs
4
Click each result to auto-fill IP, port and stream path
METHOD B — Manual Discovery Tools
ONVIF Device Manager:
Free Windows tool. Finds all ONVIF cameras on LAN instantly.
Angry IP Scanner:
Scan subnet, look for port 554 open = likely RTSP camera.
Hikvision SADP Tool:
Hikvision-only. Shows all HIK cameras, lets you reset IPs.
Dahua ConfigTool:
Dahua-only. Finds and configures all Dahua cameras on LAN.
Camera Inventory Worksheet — Complete One Row Per Camera
Cam ID | Brand/Model | IP Address | Zone | RTSP Port | Username | Status
CAM-001 | Hikvision DS-2CD2143 | 192.168.10.101 | Welding Bay A | 554 | admin | ⬜ Pending
CAM-002 | Dahua IPC-HDW2831T | 192.168.10.102 | Assembly Line | 554 | admin | ⬜ Pending
CAM-003 | CP Plus CP-UNK-1080 | 192.168.10.103 | Paint Zone | 554 | admin | ⬜ Pending

## Slide 10
SAFEG AI
03 — CAMERA DISCOVERY
10 / 24
DISCOVERY
Step 2 — Camera Health & Compatibility Audit
For each discovered camera, verify these 5 health checks before connecting to SafeG AI:
1
Verify RTSP Stream Accessible
Open VLC → Media → Open Network → Enter rtsp://admin:PASSWORD@CAMERA_IP:554/stream1
If video plays → RTSP is working. If not → see Troubleshooting slide.
✓ Video plays in VLC
✗ Connection refused / timeout
2
Check Video Resolution & Frame Rate
In camera web UI → Video → Encoding: Confirm main stream is ≥ 720p, H.264 or H.265 codec, ≥ 5 FPS.
✓ 720p+ at 5+ FPS
✗ Sub-stream only or < 5 FPS
3
Confirm ONVIF is Enabled
Camera web UI → Network → Advanced → ONVIF: Enable ONVIF service. Set authentication to Digest/WS-Security.
✓ ONVIF status: Active
✗ ONVIF disabled (enable it)
4
Test Camera Field of View
View live feed — confirm the camera covers the work area you want to monitor. Entire PPE zone must be visible in frame.
✓ Full zone visible
✗ Partial coverage → remount
5
Verify Lighting Conditions
Check feed at shift start (worst light). Min 200 lux. If IR/night-vision active, check AI can see worker features.
✓ Workers clearly visible
✗ Too dark → add IR light

## Slide 11
04
SafeG AI Account
& Wizard Setup
Create your SafeG account, register your plant, zones and existing cameras
SAFEG AI
SECTION 04 — ACCOUNT & WIZARD SETUP
11 / 24

## Slide 12
SAFEG AI
04 — ACCOUNT & WIZARD SETUP
12 / 24
ACCOUNT SETUP
Creating Your SafeG AI Account & Completing the Wizard
Go to app.syyaimsafeg.ai → Sign Up → Complete 5 wizard steps:
1
Company Details
Company name, CIN, industry
GSTIN, registered address
Primary contact + designation
2
Plant / Factory
Plant name & address
Factory Licence Number
GPS co-ordinates
3
Zones / Areas
Add zone (Welding, Assembly…)
Set PPE rules per zone
Mark danger zones
4
Register Cameras
Enter camera details from audit
RTSP URL or IP per camera
Map each cam to a zone
5
Activate
Review all settings
One-click activation
Cameras stream live
⚡ Step 4 is where you enter RTSP URLs for your existing cameras. Have the Camera Inventory Sheet from Step 3 ready.

## Slide 13
05
Connecting Cameras
to SafeG AI
Three connection methods — step-by-step for every camera brand
SAFEG AI
SECTION 05 — CONNECTING CAMERAS
13 / 24

## Slide 14
SAFEG AI
05 — CONNECTING CAMERAS
14 / 24
CONNECTION
Three Ways to Connect Your Existing Cameras
Method A
Direct RTSP URL
Best for: All brands when you know the camera IP
1
Confirm camera RTSP port (default 554)
2
Build URL: rtsp://USER:PASS@IP:PORT/PATH
3
In SafeG wizard → Camera → 'Add Manually'
4
Paste RTSP URL → Click 'Test Stream'
5
Green tick = live stream confirmed → Save
Fastest method — works with any RTSP camera
Method B
ONVIF Auto-Connect
Best for: Any ONVIF-compliant camera on LAN
1
Ensure ONVIF is enabled in camera web UI
2
In SafeG wizard → Camera → 'Scan ONVIF'
3
Select camera from discovered list
4
Enter admin credentials when prompted
5
SafeG pulls stream URL automatically → Save
Easiest — SafeG auto-discovers compatible cams
Method C
Brand SDK / NVR
Best for: Hikvision / Dahua behind NVR
1
For NVR: Use NVR IP instead of camera IP
2
RTSP path: /Streaming/Channels/101 (cam 1)
3
For Hikvision ISAPI: SafeG SDK mode in Settings
4
Enter NVR IP, port 8000, credentials
5
Select channels to connect → Activate
Use when cameras are managed through an NVR

## Slide 15
SAFEG AI
05 — CONNECTING CAMERAS
15 / 24
RTSP REFERENCE
RTSP URL Reference — Brand by Brand
URL Structure:
rtsp://
USER:PASS
@
CAMERA_IP
:554/
STREAM_PATH
Brand | Main Stream RTSP URL | Sub-Stream URL | Notes
Hikvision | rtsp://admin:PASS@IP:554/Streaming/Channels/101 | rtsp://admin:PASS@IP:554/Streaming/Channels/102 | 101=main, 102=sub-stream
Dahua | rtsp://admin:PASS@IP:554/cam/realmonitor?channel=1&subtype=0 | rtsp://admin:PASS@IP:554/cam/realmonitor?channel=1&subtype=1 | subtype 0=main, 1=sub
Axis | rtsp://root:PASS@IP/axis-media/media.amp | rtsp://root:PASS@IP/axis-media/media.amp?resolution=640x480 | Use VAPIX stream
Bosch | rtsp://IP:554/rtsp_tunnel?h26x=4&line=1&inst=1 | rtsp://IP:554/rtsp_tunnel?h26x=4&line=1&inst=2 | No credentials in URL
CP Plus (CPDI) | rtsp://admin:PASS@IP:554/live/ch00_0 | rtsp://admin:PASS@IP:554/live/ch00_1 | ch00 = channel 1
Hanwha/Samsung | rtsp://admin:PASS@IP/video1 | rtsp://admin:PASS@IP/video2 | Sunapi also available
Reolink | rtsp://admin:PASS@IP:554/h264Preview_01_main | rtsp://admin:PASS@IP:554/h264Preview_01_sub | Enable RTSP in camera settings first
Generic ONVIF | rtsp://admin:PASS@IP:554/onvif1 | Use ONVIF Device Manager to get exact path | Path varies by firmware

## Slide 16
SAFEG AI
05 — CONNECTING CAMERAS
16 / 24
NVR / DVR
Connecting Cameras Behind an NVR or DVR
Many plants have cameras connected to a Network Video Recorder (NVR) — follow these steps:
IP Camera ×N
NVR / DVR
LAN Switch
SafeG AI
Server
SafeG AI
Cloud
RTSP pulled per channel from NVR IP (not individual camera IPs)
NVR RTSP Channel URL Patterns
Hikvision NVR:
rtsp://admin:PASS@NVR_IP:554/Streaming/Channels/101
(channel 1 main), /201 (ch2), /301 (ch3)…
Dahua NVR:
rtsp://admin:PASS@NVR_IP:554/cam/realmonitor?channel=1&subtype=0
Change channel=2, channel=3… for each cam
Generic NVR:
rtsp://admin:PASS@NVR_IP:554/stream1?channel=1
or use ONVIF Device Manager on NVR IP
NVR Integration Tips
Use NVR IP address — not individual camera IPs
Each channel = one camera. Channel 1 = first camera in NVR
Confirm NVR has RTSP enabled (some older DVRs block it)
NVR must be on same network segment as SafeG AI server
Port 554 (RTSP) must be open on NVR firewall
If NVR has access control, whitelist SafeG server IP

## Slide 17
SAFEG AI
05 — CONNECTING CAMERAS
17 / 24
CAMERA SETTINGS
Enabling RTSP & ONVIF — Camera Web UI Guide
Some cameras ship with RTSP disabled. Follow these steps to enable it for each brand:
🔴 Hikvision
1
Open browser → http://CAMERA_IP → Login as admin
2
Configuration → Network → Advanced Settings → Integration Protocol
3
Enable Hikvision-CGI → Enable ISAPI → Save
4
Configuration → Network → Advanced → RTSP: Enable RTSP auth
5
RTSP port: confirm 554 → Apply
🔵 Dahua
1
Open browser → http://CAMERA_IP → Login as admin
2
Setup → Network → Connection → RTSP: Enable → Port 554
3
Setup → System → General → ONVIF: Enable → Create ONVIF user
4
Set ONVIF user same as camera admin credentials
5
Save and reboot camera if prompted
🟠 Axis
1
Open browser → http://CAMERA_IP → Login
2
Settings → System → Plain Config → Network → RTSP
3
Confirm RTSP enabled → Port 554 → Save
4
Settings → System → ONVIF → Enable ONVIF service
5
Add ONVIF user under Settings → System → Users
🟢 CP Plus
1
Open browser → http://CAMERA_IP → Login as admin
2
Configuration → Network → Port: confirm RTSP 554
3
Configuration → Network → ONVIF: Enable ONVIF
4
Note: Default stream path: /live/ch00_0 (main)
5
Reboot after enabling ONVIF for changes to apply
💡 After enabling RTSP/ONVIF, always test with VLC first before entering URL in SafeG AI wizard.

## Slide 18
06
Troubleshooting
& Validation
Fix the most common RTSP / ONVIF errors before going live
SAFEG AI
SECTION 06 — TROUBLESHOOTING
18 / 24

## Slide 19
SAFEG AI
06 — TROUBLESHOOTING
19 / 24
TROUBLESHOOTING
Common RTSP Errors & How to Fix Them
❌ Connection Refused / Timeout
Cause: RTSP not enabled or wrong IP/port
1. Ping camera IP — if no reply, check network cable/switch
2. Verify RTSP port is 554 (check camera settings)
3. Ensure port 554 open on any firewall between server and camera
4. Try: telnet CAMERA_IP 554 — should connect
❌ 401 Unauthorized
Cause: Wrong username or password in RTSP URL
1. Open camera web UI to confirm login credentials
2. Some cameras need a separate RTSP user (create one in camera settings)
3. Avoid special characters in password in URL — use URL encoding if needed
4. Hikvision: confirm admin account is not locked after failed attempts
❌ Black Screen / No Video
Cause: Stream path wrong or codec unsupported
1. Try sub-stream path (e.g. /102 for Hikvision instead of /101)
2. Set camera encoding to H.264 (some older SafeG versions need H.264)
3. Check camera main stream is not already maxed out (other NVR consuming it)
4. Use ONVIF Device Manager to get exact working stream URL
❌ Choppy / Delayed Video
Cause: Network congestion or insufficient bandwidth
1. Run iperf3 test from SafeG server to camera subnet
2. Reduce camera bitrate to 2–4 Mbps in camera settings
3. Use H.265 codec if supported — 50% less bandwidth
4. Check switch port speed — should be 100 Mbps minimum
❌ SafeG Shows Camera Offline
Cause: Camera IP changed (DHCP) or RTSP stream dropped
1. Assign static IP or DHCP reservation to every camera
2. Check camera is powered on (PoE switch LED status)
3. In SafeG Dashboard → Camera → Re-test Stream
4. Enable auto-reconnect in SafeG camera settings

## Slide 20
SAFEG AI
06 — TROUBLESHOOTING
20 / 24
VALIDATION
Live Stream Validation — Before Going Live
Stream Quality Checks
All cameras show 'Online' in SafeG dashboard
Live feed visible (no black screen) for every camera
Resolution ≥ 720p confirmed in stream info
Frame rate ≥ 3.5 FPS sustained under all-cameras load
Stream auto-reconnects after 60-second disconnect test
Coverage & Field of View
Full work zone visible in each camera frame
Workers' full body visible (not just upper body)
No blind spots where workers could stand undetected
Lighting adequate for AI — no silhouetting or glare
Camera angle confirmed for PPE detection (not top-down)
AI Detection Tests
Walk each zone wearing full PPE — zero false violations
Remove hard hat — violation detected within 3 seconds
Remove safety vest — separate violation triggered
Stand at danger zone boundary — alert fires immediately
Night/low-light test: detection works in dark shift
Alert & Integration Tests
Test violation triggers WhatsApp to HSE officer
Email alert received by all configured recipients
Dashboard violation counter increments correctly
Form 18 auto-populates from test violation data
Acknowledge → resolve workflow tested end to end
✅ All checks passed → System accepted. SafeG AI team countersigns the Go-Live acceptance form.

## Slide 21
07
AI Rules, Alerts
& Go-Live
Configure AI detection per zone, set up WhatsApp alerts and go live
SAFEG AI
SECTION 07 — AI RULES & GO-LIVE
21 / 24

## Slide 22
SAFEG AI
07 — AI RULES & GO-LIVE
22 / 24
AI CONFIGURATION
Configuring AI Detection Rules Per Zone & Camera
PPE DETECTION — WHAT AI MONITORS
⛑
Hard Hat / Helmet
detect_helmet
ON
🦺
Safety Vest
detect_vest
ON
👟
Safety Boots
detect_boots
OFF
🥽
Eye Protection
detect_eye
OFF
🧤
Gloves
detect_gloves
OFF
🚧
Danger Zone Entry
detect_zone
ZONE
🎧
Ear Protection
detect_ear
OFF
📡
Motion / Presence
detect_motion
ON
SENSITIVITY & ALERT SETUP
HIGH
Alert every detection
Best: Welding, Chemical
MEDIUM
Alert after 2 detections
Best: Assembly, Machine
LOW
Alert on repeated offence
Best: Entry points, Canteen
ALERT CHANNELS
📱 WhatsApp:
Add HSE mobile in Settings → Alerts
📧 Email:
Add emails in Settings → Email
🖥️ Dashboard:
Auto — no config needed
📋 Form 18:
Auto-populates from violations
Example — Zone AI Rule Configuration
Zone | PPE Required | Sensitivity | Danger Zone
Welding Bay | Helmet, Vest, Gloves, Eye, Ear | HIGH | Yes
Assembly Line | Helmet, Vest, Boots | MEDIUM | No
Paint Booth | Helmet, Vest, Eye, Respirator | HIGH | Yes
Machine Shop | Helmet, Vest, Boots, Eye | MEDIUM | No

## Slide 23
SAFEG AI
07 — AI RULES & GO-LIVE
23 / 24
GO-LIVE
Go-Live Day Plan & Form 18 Compliance Workflow
🚀 Go-Live Day Schedule
08:00
SafeG AI team performs final stream test — all cameras green
09:00
AI detection rules activated — monitoring begins
09:30
HSE Officer verifies WhatsApp + Email alerts with test event
10:00
First full shift under live AI monitoring
16:00
End-of-shift review: violations, heatmaps, camera uptime
17:00
Form 18 first auto-draft reviewed by HSE Officer
📋 Form 18 Auto-Workflow
1
AI auto-populates 94% of Form 18 fields
2
HSE Officer reviews & corrects if needed
3
Plant Manager approves digitally
4
PDF generated — inspector-ready format
5
Archived in SafeG reports vault (7 years)
📞 Support Contacts During Onboarding
WhatsApp 24×7
+91 98765 43210
Instant response
Email Support
support@syyaimsafeg.ai
< 4 hr response
Onboarding CSM
Dedicated manager
Business hours
Emergency Hotline
+91 98765 43220
Critical 24×7

## Slide 24
SAFEG AI
Your Existing Cameras
Are Now Live.
SafeG AI is now protecting your workers 24/7 — using the cameras you already own,
no new hardware, no downtime, no disruption.
🖥 Dashboard
app.syyaimsafeg.ai
🛟 Support
support.syyaimsafeg.ai
📚 Docs
docs.syyaimsafeg.ai
📱 WhatsApp
+91 98765 43210
Your SafeG AI onboarding team is available 24×7 for your first 30 days — call anytime.
Version 1.0 · Confidential · © 2025 Syyaim SafeG AI Pvt. Ltd.
24 / 24